## Slide 1: Lecture 3. Plumbing
By: Dinaol

## Slide 2: In this Lecture
Introduction to plumbing work
Plumbing hand tools and Materials
Plumbing fixtures and their installations

## Slide 3: 3.1 Introduction
Plumbing includes the practice, materials and fixtures used in the installation, maintenance, extension, and alteration of all piping, fixtures, appliance, and all appurtenances in connection with any of the following:
  Sanitary drainage or storm drainage facilities,
  the venting systems and the private water supply systems,
  within or adjacent to any building, structure or conveyance; and the practice and materials used in the installation, maintenance, extension, of the storm water, liquid waste and the water supply system of any premises to their connection with any point of public disposal or other acceptable terminal.

## Slide 4: 3.1 Introduction …
Plumbing can be categorized into two main classes: water supply and wastewater plumbing.
  These categories have their own principles, materials, tools and related techniques to deliver water or to dispose the by-product to appropriate places in a sanitary manner.

## Slide 5: 3.1 Introduction …
The importance of safe methods of sewage collection, and disposal, and provision of safe water supply are realized by all sanitarians.
One of the links of this chain is the house drainage system, in other words, the plumbing system. Its importance is enhanced by the fact that it is in far closer contact with everyday life of the citizen than is the common sewer or sewage treatment plant.
The sewage, which the plumbing system carries, is potentially dangerous in that it frequently contains disease-producing bacteria. Leakage in plumbing systems, therefore, is a means to health in the house where well water supplies may be contaminated

## Slide 6: 3.2 Plumbing Tools and Materials A. Plumbing Tools
1. Plumbing tools for measuring:
  Marking pen
  Plumb level
  Sprit level
  Flange square
  Fold meter
  Caliper
  Tape meter

## Slide 7: A. Plumbing Tools …
2. Plumbing tools for threading:
  Threading die
  Die stock from 3/8 to 1 ¼ “
  Internal threading tools
  Adjustable threading tools

## Slide 8: A. Plumbing Tools …
3. Plumbing tools for cutting:
  Steel pipe cutter
  Chain cutter
  Sharp chisel
  Hacksaw
  Holesaw
  Reamer

## Slide 9: A. Plumbing Tools …
4. Plumbing tools for bending:
  Bending machines
  Bending spring

## Slide 10: A. Plumbing Tools …
5. Plumbing tools for drilling:
  The BI hand driving machine
  Manual hand driving machine
  Brick chisel
  Concrete chisel

## Slide 11: A. Plumbing Tools …
6. Other instruments for plumbing work:
  Adjustable spanner
  Adjustable wrench
  Chain wrench
  Pipe vise

## Slide 12: B. Plumbing Materials
1) Pipes
  Pipes used for rural and urban water supply and wastewater disposal projects are pressure pipes, and are usually manufactured from plastics, galvanized steel or asbestos, cement and copper pipes.
  Each material has particular advantages and disadvantages.
  When two or more materials are suitable for a given situation, the selection will be based on cost.

## Slide 13: B. Plumbing Materials …
Choice of pipe materials depends on:
  1. Required strength
  2. Corrosion resistance
  3. Erosion resistance
  4. Roughness factors
  5. Cost effectiveness

## Slide 14: B. Plumbing Materials …
Kinds of pipes used for water supply system
Steel pipes
  It is the most common employed pipe, normally connected to fittings by threaded joints.
  It is manufactured in 21-ft length and the fittings are factory threaded.
  Screwing pipe and fittings together makes joints.
  The steel pipe is the strongest pipe and the most rigid of the piping materials.
  Its cost is low, easily maintainable, easily portable, and a wide range of sizes are available.

## Slide 15: B. Plumbing Materials …
2. Plastic pipes:
  For most projects it will be found that plastic pipe will prove the most suitable.
  While there are a number of different types of plastic pipe, rigid PVC is the most commonly used, though high density polyethylene is frequently used when long lengths of small diameter pipe are required.

## Slide 16: B. Plumbing Materials …
Apart from being highly competitive in purchase price, its extreme lightness makes site handling easier and, once laid, it presents no problems of corrosion or encrustations.
A further advantage is that, due to its low friction losses, it is usually possible to use PVC pipes one size smaller than a metal pipe for the same flow and head loss conditions.

## Slide 17: Major Advantages and Disadvantages of Plastic Pipes.
Advantages
  1. Low costs, capital, transport and laying
  2. Lowest friction loss of all water pipe material
  3. Non-corrosive
  4. Non-toxic
  5. Good insulation
  6. Low thermal conductivity
  7. Rapid and simple jointing
  8. Good for laying under water
  9. Flexible
  10. Extremely light and easy to handle

## Slide 18: Major Advantages and Disadvantages of Plastic Pipes.
Disadvantages
  1. Brittle at certain temperatures
  2. Loss of strength at high temperature
  3. Not suitable for laying above ground
  4. Requires ample ground cover to avoid damage
  5. Can deform during storage

## Slide 19: B. Plumbing Materials …
Copper tubing
  It is the most expensive material used for the transportation of water and gases.
  It is non-corrosive with most water and used extensively in better grade houses.
  Also used where ground water is highly corrosive to well pipes.

## Slide 20: B. Plumbing Materials …
Galvanized steel pipe
  It is important to install under heavy loads, exposed as on bridges and lines under pressure.
  Pipe sizes are usually expressed as nominal diameter (in inches).
  The sizes normally used for small water supplies are ½’’, ¾’’, 1’’, 1 ¼ ‘’, 1 ½ ‘’, 2’’, 2 1/2 ‘’ and 3’’.
  Galvanized steel pipes are jointed by means of sockets; the pipe has a toper thread while the socket has parallel thread. Most pipes are zinc galvanized.
  However, ungalvanized or black pipe is available (primarily as well casing). Pipes are usually welded. These are somewhat cheaper than seamless pipes, and the former are entirely suitable for small community water supplies.

## Slide 21: Major Advantages and Disadvantages of Galvanized Steel Pipes
Advantages
  1. Robust but may bend
  2. Easy to lay and joint
  3. May be laid to above ground
  4. Generally unaffected by climatic conditions
  5. Fittings inexpensive extremes

## Slide 22: Major Advantages and Disadvantages of Galvanized Steel Pipes
Disadvantages
  1. Liable to internal and external corrosion
  2. Liable to incrustation
  3. Higher friction head losses
  4. Relatively high cost of purchase
  5. Relatively high cost of transport

## Slide 23: B. Plumbing Materials …
Asbestos - cement pipes
  pipe comes in greater length, therefore has fewer joints; it has a smooth surface, is noncorrosive and easily jointed, and resistant to electric current and concentrated salts.
  The more common joint is asbestos cement sleeve joint incorporating two rubber rings.

## Slide 24: Major Advantages and Disadvantages of Asbestos - Cement Pipes
Advantages
  1. Durability (known to exceed 50 years)
  2. Immunity from corrosion
  3. Low friction (low head loss)
  4. Good thermal insulation
  5. Lighter and cheaper than metal pipe
Disadvantages
  1. Liable to damage in transit.
  2. Not suitable for laying above ground or in rocky ground
  3. Supplied in relatively short lengths, hence more joints
  4. Asbestos can be very hazardous to your health

## Slide 25: 2. Fittings in water supply
Fittings in water supply are devices used to connect or bend or reduce/ enlarge or close pipes that serve different purposes.
Cap:
  A fitting into which the end of a pipe is screwed for the purpose of closing the end of the pipe.
Coupling:
  A pipe fitting with inside threads only used for connecting two pipes.
Elbow:
  A fitting joining two pipes at an angle.
Plug:
  A pipe fitting with outside thread and projecting head, often square, that is used for closing the opening in another fitting.

## Slide 26: 2. Fittings in water supply
Reducer:
  A pipe fitting with inside threads, larger at one end than at the other. All such fittings having more than one size are reducers because of the custom of stating the larger size first.
Trap:
  A fitting constructed with a water seal that, when placed in a drainage pipe, will prevent the passage of air or gas through the drainage pipe but will not prevent the flow of liquids through it.

## Slide 27: 2. Fittings in water supply
Union:
A fitting used for joining the ends of two pipes neither of which can be turned. There are two kinds of unions.
  Tee:
    An internally threaded fitting that is used to distribute pipes with a "T’’ mode.
  Cross Tee:
    an internal threaded tee that is used for distributing pipes across the four sides by making an angle of 900.

## Slide 28: 2. Fittings in water supply
Nipple:
  a short piece of pipe with outside threads used for connecting pipes or fittings in threaded joints.
Y- branch:
  an internally threaded fitting used to distribute a pipe in a “Y” shaped mode.

## Slide 29: 3. 3 Drainage and Sewerage Line System
A prerequisite to sound design of a distribution system is a complete survey covering all streets and showing elevation of all-important points.
From this survey, a map is prepared on a scale to show streams, important geographical features and adjacent areas likely to require services during the design period, and proposed as well as present streets.
With the aid of this map, the principle features of the system can be planned.
These maps also show the exact locations of the pipes in the streets.

## Slide 30: A. Some Appurtenances in Sewerage System
Manhole:
  It is important when there is:
    • change in direction.
    • change of size of diameter pipes.
    • a junction.
    • a need of cleansing.
    • a need for inspection

## Slide 31: A. Some Appurtenances in Sewerage System
Manholes should be placed at distances of not more than 110m on long straight lengths.
This distance may be increased in the case of large sized sewers.
The reason is for maintenance and installation. In addition these requirements are primarily to facilitate rodding when blockages occur.
Sometimes, it is believed that 110m is too large for small diameter pipes and one should provide manholes at 80m intervals on straight lengths.

## Slide 32: A. Some Appurtenances in Sewerage System
Waste pipes
There are different pipes that can be used for the conveyance of wastewater from the source of generation to the final disposal site.
Some of the common types are:

## Slide 33: Waste pipes
1. Concrete pipe
For small and medium size sewers, up to 24’’ in diameter, the use of non-reinforced concrete pipe is generally economical.
If it is properly manufactured, it is highly resistant to weathering, chemicals (except acids) and wear.
Acids should in general be kept out of sewers or neutralized.

## Slide 34: Waste pipes
2. Cast iron pipe
It has a long life span, provide good flow characteristics, has the ability to withstand high internal pressures and external loads, and is corrosion resistant in most soils.

## Slide 35: Waste pipes
3. Plastic pipe
It is rapidly increasing in popularity because of its light weight, and ease of handling and assembly.
Although such pipe is becoming widely available, its uncertain life tends to prevent its widespread use for sewers.
It is also free from corrosion, has good resistance to shock, acids and sunlight or bad weather, has flexibility, etc.

## Slide 36: Waste pipes
4. Asbestoses- cement pipes
These pipes are highly subjected to corrosion.
However, they are low in cost, watertight, have low infiltration, and good flow characteristics, and are lightweight and easy to handle and cut.

## Slide 37: B. Construction of sewer pipe
Inspection is perhaps the most important part of sewer construction.
The pipe is generally tested under inspection and marked before delivery to the job.
Aside from quality of the finished products there are other important reasons:
  For close inspection safety
  To control pollution of groundwater
  To know the foundation is adequate
Concrete support is the best support for sewer pipes where good natural foundation does not exists. What goes around and over the sewer pipe is as important as the support under it.
Back filling is a vital operation. Fill should be placed and tamped equally and carefully on each side to at least 2 ft above the top of sewer.

## Slide 38: B. Construction of sewer pipe
Vent pipes:
are installed to provide a flow of air to or from a drainage system (pit). It also provides circulation of air within such a system to protect traps of backpressure. The various
types of materials that are used for vent pipes are:
  PVC tubing
  Masonry works
  Plane sheet metals

## Slide 39: B. Construction of sewer pipe
Size of pipes depends on:
  The size of waste
  Number of fixtures
  Number of closets connected.
Smaller diameter pipes are prohibited because it may restrict venting action. The vent size should not less than 1 ¼ inches in diameter.

## Slide 40: Fixture:
is a receptacle attached to a plumbing system other than a trap in which water or wastes can be collected or retained for use and for proper discharge into the drains.
Water closet (W.C.):
The water closet, popularly known in its abbreviated form the W.C., is a device for depositing human wastes directly into a properly designed bowl or pan.
Then the excreta are immediately carried away by water, which is flushed under pressure.
These pans are designed in connection with flushing water under pressure.

## Slide 41: Fixture:
2. Flushing cistern:
  The flushing cistern attachment is designed to release a predetermined quantity of water under pressure in order to flush away excreta from W.C. pans or urinals.

## Slide 42: Fixture:
3. Lavatory:
  is a fixture designed for the washing of the hands and face, sometimes called a washbasin. These, like other sanitary fittings, are designed in a standard form and various makes are found on the market.
  They are usually made of glazed earthenware or porcelain. At the bottom they are connected to the wastewater discharge pipe.
  Since the room containing the washbasin often contains a W.C., the lavatory is often called the W.C.

## Slide 43: Fixture:
4. Bathtub and shower:
A modern bathroom is provided with a bathtub and/or a shower for washing the body.
Here again the bath is designed in a standard form and shape. A typical bath is oval-shaped, made of glazed earthenware or enameled cast iron.
It is provided with a discharge hole controlled by a stopper or plug and chain, and fitted with an overflow device, in case the water is accidentally left flowing into the bath.
Hot and cold water faucets or taps are fitted for filling the tub. Showers may be installed together with the bathtub or separately.

## Slide 44: Fixture:
5. Bidet:
A bidet is an oval-shaped sitting-pan provided in some houses and fashionable hotels by the side of the W.C. and bathtubs.
The bidet is not an essential component of bathroom fittings. It is provided for the purpose of intimate washing, especially for women. It is furnished with hot and cold water, and can produce an upward spray as desired.

## Slide 45: Fixture:
6. Sink:
Sinks are large basins permanently installed in kitchens for washing dishes, pans, etc., and for cleaning vegetables, etc.
Sinks are provided with stoppers for keeping water in them, and with an overflow device.
They are connected through traps to the wastewater discharge pipes.

## Slide 46: Fixture:
Another sanitary fitting commonly found in a modern house is the laundry facility, for washing clothes. It is usually a large sink, or two large sinks side by side, for washing and rinsing out soap.

## Slide 47: Fixture:
Traps:
A Trap is a device or fitting so designed and constructed as to provide a filter when properly vented.
A liquid seal will prevent the back passage of air without materially affecting the flow of sewage or wastewater through it.
Trap seal is the maximum vertical depth of liquid that a trap will retain. It should have one clean-out hole.
It is used to prevent passage of sewer gas into the house system.

## Slide 48: Fixture:
Valves
The various types of valves likely to be used in different rural water supply projects are briefly described below. As these particular items are relatively expensive, care is needed in their selection.

## Slide 49: Fixture:
A. Gate Valves
  The gate valve (or sluice valve) is used to cut off flows in pipelines by lowering a solid-type wedge "gate"; during normal operation unrestricted straight-through flow is achieved as the "gate" is raised inside the valve body (referred to as the bonnet), so that the bore of the pipe is completely clear.

## Slide 50: Fixture:
B. Butterfly Valves
The butterfly valve performs a function similar to that of the gate valve; its principle of operation is the turning of the disc through 90 degree to permit water to pass.
The claimed advantages over the gate valve are lightness, greater speed of operation, low-pressure drop and low maintenance.
Minimum size is 2" (50 mm).

## Slide 51: Fixture:
C. Globe valves
Globe valves are less efficient than gate valves or butterfly valves, as the flow of water through them is not "straight", and thus greater head losses are induced.
They are, however, cheaper, and in sizes up to 2" (50 mm) could be suitable for rural water supply pipelines.
These valves are supplied complete with hand-wheels and have either double female threaded ends or double flanged ends.

## Slide 52: Fixture:
D. Check Valves
Check valves close automatically when a reversal of flow occurs, thus preventing water from flowing back, e.g., in the case of a force main (pumping main) causing damage to the pump assembly.

## Slide 53: Fixture:
E. Air valves
Air valves are located at all high spots on a pipeline and permit the discharge of air, which is likely to accumulate there.
Such air, unless removed, induces water hammer; it can also seriously restrict the flow of water in the pipeline.
Valves have cast iron bodies. The ball is rubber covered. Ball size is selected to suit working pressure; the higher the pressure the larger the ball. These valves release air at any pressure below maximum working pressure.

## Slide 54: 3.4 Basic Techniques in Plumbing
A. Pipe Cutting
Chipped or damaged ends of asbestos-cement pipes are likely to produce non-watertight joints. Such ends should be cut off.
For small diameter pipes, the ends may be cut with a handsaw or a hacksaw.

## Slide 55: 3.4 Basic Techniques in Plumbing
Alternatively, ratchet type pipe cutters can be used, which are quicker and usually give a better result.
A single pipe cutter is available that can cut pipes from 2" to 6".
Another model is the hydraulic pipe cutter, which involves wrapping a cutting chain around the hydraulic pipe cutter and then hand-operating the hydraulic pump.
This builds up sufficient pressure on the chain to "pop" the pipe with a clean cut.

## Slide 56: 3.4 Basic Techniques in Plumbing
Steel pipes can be cut to length with metal hacksaws, but it is more usual to employ manually-operated heavy-duty pipe cutters (commonly 3 or 4 wheel type) if the pipe diameter exceeds 1- ½" (40 mm).
A half-round coarse file is used to trim the cut ends internally and externally. Both PE and PVC plastic pipe can be cut with a metal cutting saw.

## Slide 57: 3.4 Basic Techniques in Plumbing
Special pipe cutters are available for PVC pipes, usually capable of cutting pipes of several sizes, e.g. ¼" to 3 - ½" or 4" to 6" (8-90 mm or 100 - 150 mm).
For PVC pipes using cement solvent, it is helpful to the joint if both male and female ends are roughened with sandpaper.
When "rubber ring push fit" joints are used on spigot and socket pipes, and when the spigot end has been damaged, the new cut end may be filed down to the necessary chamfer.

## Slide 58: 3.4 Basic Techniques in Plumbing
B. Pipe Threading
Steel pipes are jointed by threaded couplings (sockets) or by screwed - on flanges. In either case, a cut pipe will require a new thread.
Pipe stock and die sets are available for any desired pipe thread; these sets will usually cover several pipe sizes.

## Slide 59: 3.4 Basic Techniques in Plumbing
Supplementary equipment includes a pipe vise (which can be tripod-mounted or bench-mounted), a pair of "Stillson" pipe wrenches or chain pipe wrenches and an oiling can or patent "cutting" compound to prolong the life of the tool, as well as to facilitate the operation.

## Slide 60: 3.4 Basic Techniques in Plumbing
C. Connection of pipes and fixtures
When a water supply system includes a piped distribution network, the water mains must be tapped to make a connection for such outlets as public standpipes (public fountains/public stand posts) or for “private” connections to individual houses or public buildings.

## Slide 61: 3.4 Basic Techniques in Plumbing
For galvanized steel pipes a tee is inserted in the pipeline, but for asbestos-cement it is more usual to drill a threaded hole through the pipe to receive the connection.
For the smaller diameter PVC water mains, tees can be used. For the smaller diameter mains, PVC tees are available for branch connections off the water main and should be used.
For the larger diameters, 4” (100 mm) and over, suitably sized tees are not usually available and so PVC saddles are used, as the pipe should not be directly tapped.

## Slide 62: 3.4 Basic Techniques in Plumbing
Inserting a tee with a reduced branch effects a connection to a galvanized steel pipeline; this branch can be further reduced in size by one or more reducers.
The thin wall of these pipes precludes tapping as for asbestos-cement or PVC mains. For larger size connections a saddle must be used.
This is bolted to the water main and drilling is done through a boss, which is frequently pre-drilled.
A gasket between the pipe and saddle is commonly used.

## Slide 63: 3.4 Basic Techniques in Plumbing
The connection pipe may be larger and effected by means of a reducer between the connection pipe and tapping.
These days, connection pipes are normally plastic (PVC or polyethylene).
The galvanized steel pipe is likely to have a short life, loses capacity due to encrustation and can lead to water losses due to rust or zinc spelter becoming embedded in washers and so preventing water-tight closure.

## Slide 64: 3.4 Basic Techniques in Plumbing
All outlet taps should have a stopcock on the line between the main and tap to permit repairs to the tap.
If the connection is metered, the stopcock is located downstream of the meter.
For public outlets (standpipes, fountains, etc.), the tap (faucet) may be the ordinary bib type.
This may prove better than the patented “Waste-Not” type of automatic shut-off tap, which relies on a spring for closure.

## Slide 65
End of plumbing
Next Lecture is Masonry work (Lecture 4.)