## Slide 1
to compress very large tubes. Flow rate is there- fore more limited than in other pumps. Pumping efficiency is also limited if very large pressures are required. In general, commercial peristaltic pumps can be found for flow rates up to 10 m3 h-1 and pressures up to 1.6 MPa.
Summary of Pump Selection Criteria
Table 1 provides an overview of the main selection criteria for pumps. In general practice, centrifugal pumps are used unless the fluid is too viscous, con- tains solid particles, or is too strongly affected by the high shearing and/or internal energy generation.
See also: Flow Equipment: Principles of Pump and Piping Calculations; Valves. Heat Exchangers. Process and Plant Design.
Further Reading
Davidson J (1986) Process Pump Selection: A Systems
Approach. Ipswich: Institution of Mechanical Engineers.
Engineering Equipment Users' Association (1972) Guide to the Selection of Rotodynamic Pumps. London: Engineering Equipment Users' Association.
Karassik IJ and Krutzsch WC (1986) Pump Handbook.
New York: McGraw-Hill.
Lobanoff VS and Ross RR (1992). Centrifugal Pumps: Design and Application. Houston: Gulf Publishing Co. McGuire JT (1990) Pumps for Chemical Processing.
New York: Marcel Dekker.
Perry R and Chilton C (1984). Perry's Chemical Engineers' Handbook, 6th edn. New York: McGraw-Hill.
Stepanoff AJ (1992). Centrifugal and Axial Flow Pumps:
Theory, Design, and Application. Melbourne, Australia: Krieger Publishing Co.
Wahren U (1997) Practical Introduction to Pumping
Technology: A Basic Guide to Pumps - From Specifica- tion to Installation and Operation. Houston: Gulf Publishing Co.
Walker R (1977) Pump Selection: A Consulting Engineer's Manual. Ann Arbor: Ann Arbor Science Publishers.
Yedidiah S (1996) Centrifugal Pump User's Guidebook:
Problems and Solutions. Dordrecht, The Netherlands: Kluwer.
Valves
K Cronin and D MacCarthy, University College, Cork, Ireland
Copyright 2002, Elsevier Science Ltd. All Rights Reserved
Introduction
Valves are devices for controlling the flow of fluids (liquids and gases), and in some cases granular or powdered materials. This article primarily discusses the valves used in product liquid lines in a dairy
Table 1
Selection criteria for types of pumps
FLOW EQUIPMENT/Valves
1093
Type of pump | Good for | Not good for
Centrifugal | Low-viscosity fluids | Viscous fluids
 | Clean fluids | Fluids with solid particles
 | Steady flow rate | Fluids sensitive to heat
 |  | Fluids sensitive to shearing
Piston/diaphragm | Viscous fluids | Fluids with solid particles
 | Clean fluids | 
 | High pressures | 
 | Precise pressure control | 
Rotary/lobular | Viscous fluids | Fluids with solid particles
 | Clean fluids | 
 | Fluids sensitive to shearing | 
 | Precise flow rate control | 
Single-rotor | Viscous fluids | High pressures
 | Fluids with solid particles | 
 | Fluids sensitive to shearing | 
Mono | Viscous fluids | High pressures
 | Fluids sensitive to shearing | Fluids with solid particles
Peristaltic | Viscous fluids | High pressures
 | Fluids with solid particles | High flow rates
 | Fluids sensitive to shearing | 
 | Flow rate control | 

## Slide 2
processing plant though many of the comments are equally applicable to the valves used for service fluids such as steam, refrigerant, compressed air, process water, etc. that are also present in a dairy.
Broadly speaking, valves can be classified by their purpose as being either: (1) On-off, or (2) flow regulation.
On-off valves, which include shut-off, isolation and changeover valves, have distinct positions, fully open or closed. These valves are used to stop flow or isolate part of a process.Their function is to minimize resistance to flow when fully open, and to provide tight shut-off characteristics when fully closed.
Regulating valves, on the other hand, have a flow
passage, the area of which can be changed gradually. Such valves are used to control flow rates and pres- sures at various points in the system. Flow control valves can be adjusted continuously from fully open to fully closed in order to govern the flow rate. Pressure control valves determine pressure down- stream of the valve, i.e. maintain it at some set value irrespective of the flow rate through the valve.
Principles of Valve Construction
While a wide range of valves is used in industry, there are only a limited number of basic geometries by which an opening in a pipe can be opened or closed. Almost all valves can be classified as belonging to one of three fundamental designs or their variants. These are:
Globe valve.
Butterfly valve.
Gate valve.
The globe valve (also referred to as a seat valve) consists of a rigid valve body, weir, plug and spindle (Figure 1). In the closed position, the plug rests on the valve seat in the weir. Linear upward motion of the spindle will raise the plug off the seat and open the valve. This is the most popular type of valve for dairy products.
The butterfly valve consists of a flat disc (equal in cross-sectional area to the bore of the pipe), a valve spindle and an elastomeric or plastic seal ring (Figure 2). It operates on the principle of rotational rather than linear motion. In the closed position, the disc is face-on to the flow area and seals against the seal ring. Turning the spindle rotates the disc through a quarter turn (90o) and moves it to a side-on ori- entation with respect to the pipe bore and thus allows flow. This valve has low pressure drop characteristics. The gate valve (sometimes known as the slide valve), like the globe valve, operates on the principle of linear motion of a spindle (Figure 3). A flat disc is attached to the spindle and in the closed position, it is fully extended and blocks the flow area of the pipe. Linear upward motion of the spindle will retract the gate into the valve body and permit fluid flow. This type of valve is not used in product lines in the dairy industry as it is unhygienic, though it is used for
service fluids.
Valve Flow Design
Valve flow design applies the principles of fluid mechanics to determine the flow rate and pressure drop through the valve. Other issues that are of concern include valve flow characteristic and avoid- ance of water hammer (see Flow Equipment: Prin- ciples of Pump and Piping Calculations).
Figure 1 Globe valve.
Figure 2 Butterfly valve.
Figure 3 Gate valve.
1094 FLOW EQUIPMENT/Valves

## Slide 3
Pressure Drop
All valves cause losses of head (i.e. pressure) in the system due to friction effects. In general, the smaller and more intricate the passage through which the fluid has to pass, the greater the pressure loss. Con- sidering the flow of a turbulent and incompressible liquid (liquid milk for example), the pressure loss through a valve is proportional to the square of the mean liquid velocity:
P = k
pu2
2
where P = pressure loss through the valve (Pa),
p = density of liquid (kg m-3), u = mean fluid velocity (m s-1) and k = friction factor.
Using the continuity equation, pressure drop can also be expressed in terms of the volumetric flow rate through the valve:
8kpQ2
P = 1r2D2
where Q = volumetric flow
rate (m3 s-1) and
D = valve bore diameter (m). Values for the friction
factor k of the valve depend on the exact shape of the flow passage and are generally found from experi- ment. In some cases, the pressure loss through a valve is expressed in terms of an equivalent length of un- obstructed straight piping in which an equal pressure loss would occur. Rather than this equivalent length being given as an absolute measurement in metres, it is more conventional to express it as an integer number of the pipe diameter.
Table 1 gives approximate values for the friction factor and equivalent lengths for a fully open globe valve and gate valve. It must be stressed that these figures are only a rough estimate and many unstated assumptions (such as Reynolds number of flow, valve bore diameter, pipe roughness, etc.) underlie them.
Valve Characteristic
An important design feature for modulating valves is the valve characteristic. This is the relation between the stem (spindle) position of the valve and the flow through the valve at constant pressure drop. The valve characteristic determines how a control valve regulates the flow. Two characteristics must be
evaluated for valve selection: the inherent and installed characteristics. The inherent flow charac- teristic is the relationship between valve stroke and the resulting fluid flow through it for the valve on its own. The installed flow characteristic is the actual relationship between valve stroke and flow when the valve is an element in a particular flow system. Hence, the installed flow characteristic incorporates the inherent flow characteristic of the valve itself together with the flow characteristics of the whole line, i.e. it depends upon the ratio of the pressure drop through the valve to the total pressure drop across the line and valve.
The inherent flow characteristic is the theoretical performance of the valve and is generally either linear or equal percentage. In a linear valve, the relationship between the position of the spindle and the flow rate is linear while in an equal percentage valve it is loga- rithmic. The logarithmic relationship is more useful when the pressure drop in the pipeline is very sig-
nificant compared to that caused by the valve itself, since in this case, the whole system actually has a
nonlinear response. For the control system designer, the aim is to select a valve the inherent flow charac- teristic of which gives an installed flow characteristic that makes the flow controllable over the whole range of valve movement, i.e. stem position.
Water Hammer
Sudden closure of a valve can produce the phenom- enon of 'water hammer' in the pipe system. The name is a misnomer; this problem can occur with all liquids. Water hammer occurs when the abrupt deceleration of a liquid in a pipeline, caused by closing a valve too quickly, produces transient pressure shock waves in the liquid. These shock waves in turn can lead to appreciable and damaging levels of pipe vibration. Equipment such as process vessels and heat exchangers connected to the pipe may also be exposed to this vibration. Water hammer must be avoided in the design and selection of the pipe and valve system. Valves should be installed so that valve spring force and fluid pressure force act in opposite directions. Analysis is detailed but funda- mentally it involves imposing a minimum time limit on the duration for valve closure to avoid deceler- ating the liquid too rapidly.
Valve Hygienic Design
In a dairy, of all the pipe fittings in the product line, valves are probably the most technically complex. For hygiene reasons, all wetted metal parts of the valve are made of stainless steel. These are surfaces
Table 1 Friction losses through valves
k
UD
Globe valve (wide open) Gate valve (wide open)
10
0.2
340
13
FLOW EQUIPMENT/Valves 1095

## Slide 4
that intentionally or unintentionally (e.g. by splash- ing) come in contact with the product. Two main grades are used, AISI 304 and AISI 316. The valve body and all the fittings (actuator spindle, springs, flanges, bolts, operating levers and wheels) are gen- erally made from 316 stainless steel.
Valve seals can be made from a variety of synthetic food-grade rubbers; amongst the most common types are silicone rubber, butyl rubber, nitrile rubber and ethylene propylene diene monomer (EPDM). The actual choice of rubber is determined by the par- ticular application of the seal such as required mechanical properties (particularly compression set), temperature regime, exposure to steam and cleaning/ sterilizing agents, etc.
Apart from functional performance, the most sig- nificant criterion in the selection of valves for milk processing plants is that they must be of a sanitary design and cleanable. Sanitary valves are designed according to the American 3A standards or other relevant hygienic design codes, such as the European Hygienic Equipment Design Group (EHEDG), Swedish or German DIN standards.
Valves should be self-draining, free of dead spaces and readily cleaned. They should protect the product from contamination, prevent product leakage and not allow the ingress of microorganisms. For im- proved standards of hygiene and cleanability, valves should be connected to pipelines by butt-welding or by sanitary unions. Product contact surfaces should have a surface finish of 0.8 µm Ra or better, and be free of pits, folds or crevices.
A consequence of hygienic design considerations is that globe valves and butterfly valves are the most prevalent type of valves used in the dairy industry.
Valve Actuation
The choice is between manual, pneumatic, hydraulic or electric drives to control valve position.
In general, manually operated valves are now found only in the smaller dairy plants. Automated valves have replaced them in large modern facilities though they are still used occasionally.
Pneumatic actuation is generally the first choice in the dairy industry, with either a diaphragm or piston
actuator. Spent air can be discharged directly to atmosphere and there are no sparking risks. Because air pressures are generally low (in the region of
0.7 MPa), there are upper limits on the forces that air systems can develop without resorting to im- practicably large actuators. However, as valve open-
ing/closing forces in dairy product lines are seldom of large magnitude compared to valve forces found in
bulk chemical processing, this limitation is not of great significance.
If high valve opening/closing forces need to be generated, hydraulic actuation of the valve is suitable because of the very high oil pressures that can be generated. However, arising from the possible con- tamination of product with the oil, hydraulic actu- ation is very rare in the dairy industry. It can be found in applications where there is no possibility of contact with the product.
Electric solenoid actuation is not prevalent in the industry due to the fire/explosion risk from electric sparking. Also the damp conditions that can prevail in dairies can lead to problems with electrical con- nectors. They can be used, however, to control the pneumatic actuation circuits that in turn operate the main process and cleaning-in-place (CIP) valves.
Irrespective of the actuation mechanism chosen, valves can be arranged to be normally open or normally closed according to safe practice. Two arrangements are usual:
Air closing/spring opening (a normally open (NO) valve)
Spring closing/air opening (a normally closed (NC) valve).
Air opening/air closing valves are occasionally used. In a system with pneumatic actuation, the usual configuration is that air under pressure is used to move the valve from its default (safe) state to the active state. If the pressurized air is removed, a com- pressed spring will automatically return the valve to the default state. Hence, occurrences such as electricity failure leading to a loss of compressed air need not have unwanted consequences. As an example, valves on outflow lines from silos or storage tanks will usually have the configuration of air to open and spring to close. This diminishes the pos- sibility of loss of product due to valve system failure.
Valves in Dairy Processing
The functions of valves in the dairy processing industry are summarized in Table 2. The following types of valves are used in dairy processing.
Globe Valve
The globe valve (also called seat valve or poppet valve) is operated by the movement of a valve stem which raises or lowers a plug on to a valve seat. It can be used as a shut-off valve (Figure 4) or as a changeover or divert valve (Figure 5). When used as a shut-off valve in piping systems, it should close against the flow to reduce the possibility of water
1096 FLOW EQUIPMENT/Valves

## Slide 5
hammer. If used as a tank outlet valve, it should be installed so that static liquid pressure helps to keep the valve closed. Depending on system requirements, this valve is available with up to five ports.
Butterfly Valve
The butterfly valve (Figure 6) is designed primarily as a shut-off valve, but is sometimes used for flow regulation. When fully open, pressure drop is small, which makes the valve suitable for products which require delicate handling with minimum turbulence. It is also suitable for viscous products. The butterfly valve is available in manual or automated formats.
Double-Seat Valve
Situations arise in the dairy industry in which two pipelines must be connected to allow product to flow from one pipeline to the other, or separated to prevent mixing of two fluids such as product and detergent, and to ensure product integrity by direct- ing any leaks to drain. This function can be achieved by use of three butterfly valves, three on-off globe valves, or one on-off and one changeover valve. It can also be achieved using one double-seat valve (Figure 7), which has two separate seals, one for each pipeline. Between the seals is a chamber which is connected to the atmosphere. Provision is made for in-place cleaning of this leakage chamber. To reduce the risk of a valve seat being lifted by surges in liquid pressure, this valve is available with a hydraulically balanced plug.
Constant-Pressure Valve
In the constant-pressure valve (Figure 8), compressed air acting on a diaphragm modulates the flow in the system, in response to changes in product pressure. By this means, product pressure can be maintained constant, e.g. for supply to an item of processing equipment.
Figure 4
Seat valve - Shut-off.
Product shut-off
Stop and start the flow of product
Divert flow to another pipeline Separate two fluids, e.g. product
and detergent
Adjust the pressure or rate of flow of product
Ensure that product flows in one direction only
Control the maximum pressure of a fluid
Admit air to a vessel if vacuum exceeds a preset value
Maintain the process liquid at a constant preset pressure
Product changeover Product separation
Flow regulation
One-way flow
Pressure relief
Vacuum relief
Constant pressure
Figure 5
Seat valve - Changeover.
Figure 6 Butterfly valve.
FLOW EQUIPMENT/Valves 1097
Table 2 Functions of dairy valves
Valve type Function

## Slide 6
Modulating Valve
Conceptually similar to the globe valve, the modu- lating valve (Figure 9) is used to vary product flow rate. It operates by varying the position of the valve in the orifice in the flow weir, and flow rate is re- duced as the plug is lowered towards the valve seat. It may be operated in conjunction with a flow sen- sor which detects product flow rate and a controller which adjusts the valve setting to the required flow rate.
One-Way Valve
The one-way valve or check valve (Figure 10) uses a spring-loaded seal to allow flow in one direction, and
to stop flow in the reverse direction. Fluid flow in the desired direction uses the momentum of the fluid to keep the valve open. If the direction of flow is erroneously reversed, the valve closes under the influence of the fluid and the spring, to prevent back flow.
Safety Valves
Pressure/vacuum relief valves (Figure 11) are used to ensure safe operation by limiting the maximum
Figure 8 Constant-pressure valve.
1/1
1/2
0
1/1
1/2
0
Figure 9 Modulating valve.
Figure 10 Check valve.
Figure 7 Double-seat valve.
Figure 11 Safety valve.
1098
FLOW EQUIPMENT/Valves

## Slide 7
pressure/vacuum that can develop in a system. Pressure can be controlled by air pressure or by preset compression of a helical spring. Applications include the use of a pressure relief valve downstream of a positive displacement pump, to avoid damage in the event of a flow shut-off downstream. Since many safety valves are not air-actuated, it is difficult to open them for in-place cleaning.
Air Blow Valve
Before in-place cleaning commences, product is cleared from pipelines by use of compressed air in- troduced via an air blow valve (Figure 12).
See also: Flow Equipment: Principles of Pump and Piping Calculations. Hygiene in Dairy Production and Processing. Process and Plant Design. Services in Processing Plants: Water Supply.
Further Reading
De Nevers N (1991) Fluid Mechanics for Chemical Engineers. New York: McGraw-Hill.
Luyben WL (1990) Process Modeling, Simulation and
Control for Chemical Engineers. New York: McGraw- Hill.
Pearson GH (1978) Valve Design. London: Mechanical Engineering Publications.
Tetra Pak (1995) Dairy Processing Handbook. Lund, Sweden: Tetra Pak Processing Systems AB.
Timperley DA (1993) Hygienic design of closed equipment
for the processing of liquid food. Trends in Food Science and Technology 4: 375-379.
Figure 12 Air blow valve.
FOOD ADDITIVES
Legislation
P Berry Ottaway, Berry Ottaway & Associates Ltd,
Hereford, England
Copyright 2002, Elsevier Science Ltd. All Rights Reserved
Introduction
The addition of chemical substances to food for technological purposes, such as preservation, or for organoleptic purposes, such as colour and flavour, can be traced back over millennia. Salt was valued in early civilizations not only as a condiment but also
Contents Legislation Safety
Adverse Reactions to Additives
FOOD ADDITIVES/Legislation 1099
Other valves used in the dairy industry include flow splitters, mixing valves, sampling valves and plug cocks (for manual operation only).
Folic Acid see Vitamins: Folates, Nutritional Signifcance.