## Slide 1: 5. SOURCE PROTECTION

## Slide 2: Multiple Barrier Approach
Catchment
Source
Treatment
Distribution
Safe drinking
water

## Slide 3: Source Assessment and Protection
Location of drinking water source
Delineation of source areas and protection zone
Physical barrier effectiveness list
Inventory of contaminant sources
Assessing hazards and prioritizing risks
Source protection measures

## Slide 4: Inventory of contaminant sources
Purpose is to identify the existence and proximity to the water source of past, present and proposed activities that might be a potential threat to the water supply.
Review of information on potential contaminant sources
Conduct a contaminant source survey

## Slide 5: Sources of water pollution
POINT SOURCES
NONPOINT SOURCES
Power plants:
Heated water
Feedlots
Organics, solids, nutrients, microorganisms
Industries
Organics, chemicals, color and foam, salts, toxins, heated water
Municipalities
Domestic wastewater: Microorganisms, nitrogen, phosphorus
Water body
T
T
T
Agricultural runoff
Sediments, fertilizers, pesticides, organics, microorganisms
Mining
Suspended solids, acid-mine drainage
Urban runoff
Litter, sediments, organics, nitrogen, phosphorus, heavy metals, petroleum substances, microorganisms

## Slide 6: Factors influencing susceptibility to contamination in source area
Physical integrity of works supplying water
Physical, geologic, hydrologic, chemical, and biological characteristics that influence source water and contaminant flow to the supply point
Type, number and locations of potential contaminant sources and land use within the assessment area of a water supply
Nature and quantity of contaminants that have been or potentially could be released within a source area; the measures in place to prevent such releases

## Slide 7: Contaminant source- Required information
Time of travel from release point to intake
  Release location
  Stream velocity, discharge
Type and characteristics of contaminant
Release type: continuous or instantaneous
Concentration of contaminant at intake point
Contaminant transport mechanism
Transformation processes that may lower contaminant concentration

## Slide 8
Abstraction Point
PZ1
PZ2
PZ3
A
B
C
Surface Water Protection Zones (PZ)
Groundwater Well Head Protection Areas (WHPA)

## Slide 13
Urbanization – Shewa Robit : GW
Upstream – Dessie :Tossa Spring
Downstream – Logia : GW

## Slide 14: Assessing hazards
Biological: bacteria, viruses, protozoa, etc.
Chemical: example
Physical: sediment
Radiological
Hazard
Hazardous event
Risk

## Slide 15: Risk analysis

## Slide 16: Example- Hazard assessment

## Slide 17: Surface water pollution control methods
Pollution prevention
  Source reduction: input changes, processes changes, product changes
  Recycling/reuse, water conservation
  Minimizing illicit wastewater discharge
  Improving solid waste management, etc.
  Regulate rate, frequency and amount of fertilizer application
Reducing waste after generation
  Conventional wastewater treatment
  Alternative treatment methods
Increasing assimilative capacity of a watercourse
  Low flow augmentation
  Artificial reaeration

## Slide 18: Surface water pollution control methods…
Making better use of assimilative capacity of a watercourse
  Regulated discharge, i.e., to temporarily store water during low flow period and to release it later when flow is high.
  To collect individual effluents to a common treatment plant and discharge it at a point where impact on quality is minimized.
Landuse planning
  Zoning
  Restrictions on population density and settlement on sensitive areas
  Erosion control
  Reducing impervious surfaces
  Reducing directly connected impervious surfaces
  Low impact land development

## Slide 19: Reducing waste after generation
Treat wastewater to the required level before discharging into the receiving water system
Typical characteristics of domestic wastewater
Constituent | Weak (mg/L) | Medium (mg/L) | Strong (mg/L)
Alkalinity (as CaCO3) BOD5 Suspended solids TDS TKN (as N) Total phosphorus (as P) | 50 100 100 200 20 5 | 100 200 200 500 40 10 | 200 300 350 1000 80 20

## Slide 20: Conventional wastewater treatment
  Pretreatment – removes materials that can cause operational problems, equalization optional
  Primary treatment – remove ~60% of solids and ~35% of BOD
  Secondary treatment – remove ~85% of BOD and solids
  Advanced treatment – varies: 95+ % of BOD and solids, N, P

## Slide 21: Biological wastewater treatment
Biological secondary treatment
Suspended growth
Attached growth
Dual biological
Activated sludge
Stabilization ponds
Aerated lagoons
Containment ponds
Constructed wetlands
Plug flow
Complete mix
Oxidation ditch
Contact stabilization
Sequencing batch reactors
Conventional
Extended aeration
High rate
Step feed
Tapered aeration
Trickling filters
Biotowers
Rotating biological contactors

## Slide 22: Biological Nitrogen removal
Denitrification
BOD + Nitrification
Return nitrate
Return sludge
WAS
Anoxic tank
Aerobic tank
Secondary clarifier
Influent
Effluent

## Slide 23: Biological Nitrogen removal
BOD + Nitrification
Denitrification
Return nitrate
Return sludge
WAS
Anoxic tank
Methanol
Influent
Effluent
Aerobic tank
Aeration
WAS
Nitrification in aerobic environment
Organic matter + O2  NH3 + CO2 + microorganisms
NH3 + 2O2  NO3- + H+ + H2O + microorganisms
Denitrification in an anoxic environment (no free oxygen)
Organic matter + NO3-  N2 + microorganisms

## Slide 24: Two-stage biological P removal
Return sludge
WAS
Anaerobic tank
Aerobic tank
Secondary clarifier
Influent
Effluent

## Slide 25: Alternative Treatments
Waste Stabilization Ponds
Comprises series of man-made shallow ponds
They can achieve any required degree of treatment at the lowest cost and with minimum of maintenance by unskilled operators
The removal of pathogens is considerably greater than that in other methods of sewage treatment
They are well able to withstand both organic and hydraulic shock loads
They can effectively treat a wide variety of industrial and agricultural wastes
They can easily be designed so that the degree of treatment is readily altered
The method of construction is such that, should at some future time the land be required for some other purpose, it I easily reclaimed
The algae produced in the pond are potential sources of high-protein food which can be conveniently exploited by fish farming

## Slide 26: Waste stabilization ponds
F
M
M
M
A
F
M
M
M
Pond layouts (a) Weak-medium strength wastes (b) Strong wastes
A: Anaerobic pond F: Facultative pond M: Maturation pond
a
b

## Slide 27: Functions and requirements of ponds
Pond | Main function | Design factors
Anaerobic Facultative Maturation | Treat strong organic waste (70% reduction in BOD5) BOD removal Fecal coliform removal (99.9%) | Depth: 2-4 m Detention time: 5 days Temp/pH: > 15°C/>6 Depth: 1-1.5 m Exposed to wind Large land area Desludging: 10-15 years Depth: 1-1.5 m
Processes in a facultative pond

## Slide 28: Alternative treatments- Septic systems

## Slide 29: Land treatment methods
Application of wastewater on the land
Plants and soil play roles in pollutant removal
Three types of application:
  Slow rate infiltration
  Rapid infiltration
  Overland flow

## Slide 30: Alternative treatments- Constructed wetlands

## Slide 31: Groundwater Quality Management
Groundwater pollution risk
Aquifer pollution vulnerability
Groundwater pollution hazard
Groundwater protection
measures
  Sensitivity to contamination determined by the natural intrinsic characteristics of the geological strata
  Probability that the groundwater in an aquifer will become polluted
  Threats posed by groundwater pollution hazard to human health

## Slide 32: Key factors in aquifer vulnerability

## Slide 33: Groundwater quality management practices
Assessing actual groundwater quality status
Prohibition of certain activities in vulnerable areas
Prohibiting the disposal of certain level of waste except in sealed facilities
Management of waste effluents
Monitoring compliance with regulations/permits
Remedial actions:
  Pumping and treating polluted groundwater
  Pumping/well injection to reverse the hydraulic gradient
  Construction of physical barriers
  Chemical or bacterial in-situ treatment of contaminated groundwater

## Slide 34: Groundwater / DRASTIC Model
Initial | Description | Interpretation
D | Depth to the Water Table | The shallower the depth ??
R | Recharge of the Aquifer | Higher Rate of Recharge
A | Aquifer Media | Highly permeable aquifer media
S | Soil Media | Depth and type of soil media
T | Topography | The flatter the topography…
I | Impact of the Vadose Zone | Soil or rock type in the unsaturated zone
C | Hydraulic Conductivity | The higher hydraulic Conductivity
Score and Weight – The higher the weighted sum.. |  | 

## Slide 35
Agricultural water pollution
Point sources
- Uncovered exercise or feeding areas
- Animal waste storage facilities
- Silage effluent handling facilities
- Pesticides storage and handling facilities
Nonpoint sources
- Agricultural production areas
- Transport agents
- Excess precipitation
-Drainage water through soil
- Wind

## Slide 36: Agricultural point source controls
Site selection
  As far as practicable from surface waters and down gradient from nearby (50 to 75 m) groundwater wells
  Suitable surface and subsurface soil conditions (low organic matter, low shrink-swell potential, good compactability and adequate bearing capacity, deep water table, etc.)
Sizing of structural facilities
  Adequate capacities to hold the pollutants (and rainwater in the case of uncovered structures)
Design and construction
  Design according to accepted engineering standards and procedures
  Use corrosion resistant construction materials
  Follow accepted construction practices

## Slide 37: Non-structural BMPs for controlling Agricultural NPSP
Education: awareness on the threats of ANPSP and importance of their control
Water management: reduce erosion and nutrient losses in runoff by minimizing or slowing water flow off fields.
Examples: contour tillage, buffer strips, diversions and terraces
Landuse
  designating areas suitable for various types of development or conservation
Erosion and sediment control for cultivated crops: focuses on minimization of exposed soil and time of exposure.
Examples: conservation cover/stabilization practices, conservation tillage, cover crop, buffer zones, critical area planting, residue use, delayed seedbed preparation, indigenous weed management, mulching, strip cropping, conservation cropping;

## Slide 38: …. BMPs for controlling Agricultural NPSP
Erosion and sediment controls for livestock areas:
Example: deferred grazing, heavy use area protection
Pesticide/nutrient control:
  Good housekeeping practices, plant and soil analyses, nutrient management plan, integrated pest management, proper application of phosphorus and nitrogen, use of natural fertilizers, leguminous plants in rotation;
Pathogens: focuses on livestock and manure management;
Proper management of solid waste

## Slide 39: Structural BMPs for controlling ANPSP
Erosion control:
  Contour farming, diversions, terracing, fencing, wind erosion control
Sediment control:
  Filter strips, grassed waterways, sediment basins
Pathogens:
  Waste storage ponds, stream crossing

## Slide 40: Leachate Control
Leachate is a water-type liquid that seeps out of a landfill
The liquid comes from rain infiltration and moisture fraction of the MSW
Has a long residence time in a landfill in a predominantly anaerobic environment
It is contaminated with organics and heavy metals- highly toxic
SRT
PR
EP
SRO
LC
Landfill

## Slide 41: Composition of typical landfill leachate
Constituent | < 2 years (mg/L) | > 10 years (mg/L)
BOD5 TOC COD TSS Organic nitrogen Ammonia nitrogen Nitrate Total phosphorus Ortho-phosphorus Alkalinity as CaCO3 pH Total hardness as CaCO3 Calcium Magnesium Potassium Sodium Chloride Sulfate Total iron | 2000-30000 1500-20000 3000-60000 200-2000 10-800 10-800 5-40 5-100 4-80 1000-10000 4.5-7.5 300-10000 200-3000 50-1500 200-1000 200-2500 200-3000 50-1000 50-1200 | 100-200 80-160 100-500 100-400 80-120 20-40 5-10 5-10 4-8 200-1000 6.6-7.5 200-500 100-400 50-200 50-400 100-200 100-400 20-50 20-200

## Slide 42: Leachate management
Liners
  Objective: To minimize infiltration of leachate into aquifer system
  Selection of liner: function of geology and environmental requirements
  - If there is no groundwater a single compacted clay layer could be sufficient
  - If groundwater pollution hazard is high use a composite liner composed of clay and geosynthetic liners
Collection systems
  accomplished by using a series of sloped terraces and a system of collection pipes
Treatment
  Recycling; evaporation; treatment + spray disposal; wetlands; treatment with domestic sewage

## Slide 43: Leachate liners

## Slide 44: Typical leachate collection system